## Slide 1: Motherboard BIOS and Troubleshooting
By
E. Thirumeni
Department of Electronics
St. Joseph’s College (Autonomous)
Trichy

## Slide 2
What is a BIOS?
basic input/output system (BIOS), also known as the System BIOS
The BIOS software is built into the PC on a non-volatile ROM and is the first code run by a PC when powered on.
BIOS software is stored on a non-volatile ROM chip on the motherboard. It is specifically designed to work with each particular model of computer
A BIOS has a user interface (UI), typically a menu system accessed by pressing a certain key on the keyboard when the PC starts. In the BIOS UI, a user can:
configure hardware
set the system clock
enable or disable system components
select which devices are eligible to be a potential boot device
set various password prompts, such as a password for securing access to the BIOS UI functions itself and preventing malicious users from booting the system from unauthorized peripheral devices.

## Slide 3
What is a POST?
It means: Power On Self Test
POST includes instructions to perform internal tests, as designed by the device manufacturer.
The Instructions are stored in ROM memory, and performed every time the computer system is started.
When the PC starts up, the first job for the BIOS is the Power-on self-test, which initializes and test system components such as the CPU, video display card, Memory, hard disk drive and other hardware. The BIOS then locates boot loader software (OS) from a hard disk or a CD/DVD, and loads and executes that software, giving it control of the PC.

## Slide 4
Beep Code: Description of Problem:
No Beeps = Short,No power, Bad CPU/MB, Loose Peripherals
One Beep = Everything is normal and Computer POSTed fine
Two Beeps = POST/CMOS Error
One Long Beep,
One Short Beep = Motherboard Problem

## Slide 5
Beep Code: Description of Problem:
One Long Beep,
Two Short Beeps
OR
One Long Beep,
Three Short Beeps = Video Problem
Three Long Beeps = Keyboard Error
Repeated Long Beeps = Memory Error
Continuous Hi-Lo Beeps = CPU Overheating

## Slide 6
There are many types of BIOS the most common ones are:
IBM POST
AMI BIOS (American Megatrends)
AWARD BIOS
Phoenix BIOS

## Slide 7
1 short beep | Normal POST - system is ok
2 short beeps | POST Error - error code shown on screen
No beep | Power supply or system board problem
Continuous beep | Power supply, system board, or keyboard problem
Repeating short beeps | Power supply or system board problem
1 long, 1 short beep | System board problem
1 long, 2 short beeps | Display adapter problem
1 long, 3 short beeps | Enhanced Graphics Adapter (EGA)
3 long beeps | Keyboard error
Standard Original IBM POST Error Codes

## Slide 8
1 Beep
A single beep from an AMI based BIOS means there has been a memory refresh timer error. The solution is often to replace the RAM in the computer.
2 Beeps
Two beeps means there has been a parity error in base memory. This is an issue with the first 64KB block of memory in your RAM. The solution is usually to replace the memory.
3 Beeps
Three beeps means there has been a base memory read/write test error. Replacing the RAM usually solves this AMI beep code.
4 Beeps
Four beeps means that the motherboard timer is not working properly. A hardware failure with an expansion card or the motherboard itself could be the cause of this beep code.
AMI BIOS POST Error Codes

## Slide 9
5 Beeps
Five beeps means there has been a processor error. A damaged expansion card, the CPU, or the motherboard could be prompting this AMI beep code.
6 Beeps
Six beeps means that there has been an 8042 Gate A20 test error. This beep code is usually caused by an expansion card that has failed or the motherboard that is no longer working.
7 Beeps
Seven beeps indicates a general exception error. This AMI beep code could be caused by an expansion card problem, a motherboard hardware issue, or a damaged CPU. Replacing the faulty hardware usually fixes the cause of this beep code.
8 Beeps
Eight beeps means that there has been an error with the display memory. This beep code is usually caused by a faulty video card. Replacing the video card usually clears this up.
AMI BIOS POST Error Codes

## Slide 10
1 Short Beep
A single, short beep from an Award based BIOS is actually an "all systems clear" notification. No troubleshooting necessary!
1 Long Beep, 2 Short Beeps
One long beep followed by two short beeps indicates that there has been some kind of error with the video card. Replacing the video card is usually the most you'll have to do to fix this one.
1 Long Beep, 3 Short Beeps
One long beep followed by three short beeps means that either the video card isn't installed or the memory on the video card is bad. Reseating or replacing the video card will typically fix the cause of this Award beep code.
AWARD BIOS POST Error Codes

## Slide 11
1 High Pitched Beep, 1 Low Pitched Beep (Repeating)
A repeating high pitched / low pitched beep pattern is an indication of some kind of CPU problem. The CPU could be overheating or malfunctioning in some other way.
1 High Pitched Beep (Repeating)
A single, repeating, high pitched beeping sound means that the CPU is overheating. You'll need to figure out why the CPU is getting too hot before this Award beep code will go away. Important: Turn your computer off immediately if you hear this beep code. The longer your CPU is running hot, the higher the chance that you'll permanently damage this expensive part of your system.
All Other Beep Codes
Any other beep code pattern you hear means that there has been some kind of memory problem. Replacing your RAM is the most you'll need to do to fix this problem.

## Slide 12
1 Beep
A single beep from a Phoenix based BIOS is actually an "all systems clear" notification. Technically, it's an indication that the POST is complete. No troubleshooting necessary!
1 Continuous Beep
CPU not inserted properly or not present.
1 Long Beep, 2 Short Beeps
One long beep followed by two short beeps indicates that there has been a checksum error. This means that there is some kind of motherboard issue. Replacing the motherboard should fix this problem.
1-1-1-1 Beep Code Pattern
Most often, it's a problem with the system memory. This Phoenix BIOS issue is usually corrected by replacing the RAM.
1-2-2-3 Beep Code Pattern
A 1-2-2-3 beep code pattern means that there has been a BIOS ROM checksum error. Need to replace the entire motherboard.
1-3-1-1 Beep Code Pattern
A 1-3-1-1 beep code pattern on a PhoenixBIOS system means that there has been an issue while testing the DRAM refresh. This could be a problem with the system memory, an expansion card, or the motherboard.
Phoenix BIOS POST Error Codes

## Slide 13
1-3-1-3 Beep Code Pattern
This usually means that there is a problem with the currently connected keyboard but it could also indicate a motherboard issue.
1-3-4-1 Beep Code Pattern
A 1-3-1-1 beep code pattern on a PhoenixBIOS system means that there is some kind of issue with the RAM. Replacing the system memory usually fixes this problem.
1-3-4-3 Beep Code Pattern
A 1-3-1-1 beep code pattern indicates some kind of issue with the memory. Replacing the RAM is the usual recommendation for solving this problem.
Phoenix BIOS POST Error Codes

## Slide 14
1-4-1-1 Beep Code Pattern
A 1-4-1-1 beep code pattern on a PhoenixBIOS system means that there is an issue with the system memory. Replacing the RAM usually fixes this problem.
2-1-2-3 Beep Code Pattern
A 2-1-2-3 beep code pattern means that there has been a BIOS ROM error, meaning an issue with the BIOS chip on the motherboard. This Phoenix BIOS issue is usually corrected by replacing the motherboard.
2-2-3-1 Beep Code Pattern
A 2-2-3-1 beep code pattern on a PhoenixBIOS system means that there has been an issue while testing hardware related to IRQs. This could be a hardware or misconfiguration problem with an expansion card or some kind of motherboard failure.

## Slide 15
GROUP DISCUSSION:
Why does the computer beep everytime during start up?
Why is it important to know different beeps when dealing with computers?
How do you know what BIOS you are using on your computer?
What is the BIOS used for and its purpose?